## Slide 1
Proteomics
Systems Biology of Human Metabolism and Gut Microbiome 1 Nov 2021

## Slide 3
Mardinoglu et. al (2018), Nature Reviews Gast & Hep, 2018
Systems Biology in hepatology

## Slide 4
Systems Biology & Systems Medicine
Evolution created enormously complicated organisms and this random and chaotic process only work in particular environment.
Over the years complicated circuits are built on top of this complex structure.
To study and understand this complexity is a challenging task.
Rube Golberg’s inventions
Number of components
Individual dynamics
Their connection
System dynamics
4

## Slide 5: What is proteomics?
Definition – Large-scale study of proteins
In daily use – Studying a protein sample using mass spectrometry

## Slide 7: Mass spectrometry-based proteomics
Top down proteomics
  Analysis of intact proteins
  Complicated MS data analysis
Bottom up proteomics
  Peptides released by enzymatic degradation
  Measures peptide-ions and their fragmentation patterns
  By far the most used approach in proteomics
Quantitative shotgun proteomics: considerations for a high-quality workflow in immunology Felix Meissner & Matthias Mann Nature Immunology
Notes: Top-down
  Analyses intact proteins and map protein fragment spectra to protein sequences.
Bottom-up
  Analyses peptides from hydrolysed proteins and map peptide spectra to protein sequences to infer their presence.

## Slide 8: Different proteomics approaches
Data-dependent acquisition proteomics (DDA or Shotgun)
  No prior knowledge needed
  MS1 quantification
Data-independent acquisition proteomics (DIA or SWATH)
  Needs spectral libraries
  MS2 quantification
Targeted proteomics (SRM, MRM, PRM, HR-MRM etc.)
  Needs assay development
  Generally hypothesis driven
  MS2 quantification
Quantitative shotgun proteomics: considerations for a high-quality workflow in immunology Felix Meissner & Matthias Mann Nature Immunology
Notes: Top-down
  Analyses intact proteins and map protein fragment spectra to protein sequences.
Bottom-up
  Analyses peptides from hydrolysed proteins and map peptide spectra to protein sequences to infer their presence.

## Slide 9: Protein identification in shotgun proteomics
Kacerovsky et al (2015) Proteomic Biomarkers for Spontaneous Preterm Birth: A Systematic Review of the Literature
  Protein digestion into peptides
  Peptide separation using liquid chromatography
  Electrospray ionization
  Full scan of peptide ions (MS1)
  Selection of the most intense peptide ions to fragment and analyze (MS2)
  Fragment ion spectra are used for peptide identification
  Protein quantification based on peptide ion intensity (MS1 level)

## Slide 10: Peptide fragmentation
Peptide ion fragmentation
  Peptide ion isolation
  Collision with inert gas
Fragmentation pattern
  Based on sequence
  Depends on collision energy
Peptide identification
  Precursor mass
  Fragmentation pattern
  Match to data base

## Slide 11: Data analysis in shotgun proteomics
Dedicated software and search algorithms (vendor specific and free software)
  Load raw data files
  Detect peptide peaks
  Match peptide fragmentation spectra against a data base
  Perform some kind of peptide/protein quantification
  Produce table of identified (and quantified) peptides or proteins
Matching peptide spectra
  Choose database to match against (species, subset of proteins)
  Choose your acceptable false discovery rate (FDR, typically 1%)
Protein quantification
  Choose quantification method (label free, isobaric tags, stable isotopes)
Unique peptide  Protein ID

## Slide 12: Proteomes are Dynamic and Complex
Mike McCoss
Extracted ion chromatogram (XIC):
Looking at a specified m/z over time
Mass spectrum (full scan):
Signals for all m/z at a certain time
Notes: Horizontal: One peptide m/z over time (extracted ion chromatogram)
Vertical: One mass spectrum at a certain time point

## Slide 13: Data Dependent Acquisition will Always Under Sample
Isotope clusters identified from a shotgun experiment

## Slide 14: How well does shotgun proteomics describe a sample?
Imagine visiting Kyoto (Japan) and visiting the tallest buildings first
Analogy Nathan Yates / Mike McCoss

## Slide 15: How well does shotgun proteomics describe a sample?
Imagine visiting Kyoto (Japan) and visiting the tallest buildings first
Analogy Nathan Yates / Mike McCoss

## Slide 16: Interference
MS1
MS2
M M+1 M+2 M+3
M: monoisotopic mass

## Slide 17: Limitations with shotgun proteomics
  “Semi-random” sampling for peptide fragmentation and identification
  Data sets with missing values
  Favors detection and quantification of high abundant proteins -> low sensitivity
  MS1 quantification generally less accurate than MS2 quantification

## Slide 18: Targeted Proteomics
Selected Reaction Monitoring (SRM)/Multiple Reaction Monitoring (MRM)
Parallel Reaction Monitoring (PRM)

## Slide 19: Targeted Proteomics
Benefits
  Data for the same peptides are recorded in every run
  More consistent data
  Easier to compare between samples (e.g. case / control)
Drawbacks
  Peptides has to be well characterized
    Ionization
    Retention time
    Fragmentation
  Tedious assay development
  Only provides data on a limited number of peptides

## Slide 20: Targeted proteomics vs. shotgun proteomics
Shotgun proteomics
  Variable sampling of peptides for fragmentation – Replicate injections can detect different peptides
  Quantification on MS1-level (peptide ions)
  Generally used in discovery studies
  Limited sensitivity
Targeted proteomics
  Predefined list of peptides to fragment – Good reproducibility
  Quantification on MS2-level (fragment ions)
  Generally used for verification of an hypothesis
  Higher sensitivity
Interleukin 6

## Slide 21: Chromatographic Peak Extraction
Quantification of one peptide analyzed in PRM

## Slide 22: MS-based Peptide Quantification
Label Free
Stable isotopes
  Metabolic labeling
  Chemical labeling
  Spiked Standards

## Slide 23: Stable isotope-labeled standards
Heavy versions of peptides or proteins
  Labeled with stable isotopes to introduce a small mass shift
  13C and 15N most common
  Heavy Lys (+8 Da) or Arg (+10Da) most commonly used
  Have identical physiochemical properties as the light peptide, e.g. retention time, ionization, fragmentation
Peptides
  Chemical synthesis
  Many kinds of modifications possible
  Added late in the sample preparation
Proteins and protein fragments
  Metabolic labeling during protein expression
  Added early in the sample prep workflow
  Are enzymatically digested together with the sample

## Slide 24: Quantification
Label free quantification
Analyte (m/z = M)
Quantification using isotope labeled standards
Sample (m/z = M).
Internal standard (m/z = M + i)

## Slide 25: Accuracy and Precision
Accuracy
  How close we are to the real concentration
  Crucial when absolute quantities are needed
Precision
  How reproducible the quantification is
  Estimated by making replicate measurements
  Coefficient of variation (CV)
Accurate and precise
Precise, but not accurate
Accurate, but not precise
Neither accurate nor precise

## Slide 26: Assay validation – Apolipoprotein SRM

## Slide 27: Assay validation – Apolipoprotein SRM
Robustness across five days for 13 proteins
  CV: 4.5-8.8 %
  Median CV: 5.9 %
  Label free CV: approx. 30 %
Label free
(Peak area)
Normalized to standard
(Peak area ratio)

## Slide 28: Assessing accuracy
Notes: Good correlation with clinical chemistry done at in the hospital lab
Different scales: g/L vs. fmol/ul
APOA1: Great accuracy (provided the clinical assay is correct)
APOB: We seem to overestimate APOB by a factor of almost 2. Is this good accuracy? Dynamic range of plasma what we can detect in plasma is 4-5 orders of magnitude

## Slide 29: Targeted proteomics data analysis in Skyline
  Add list of the analyzed peptides
  Read raw data files
  Integrate peaks (automatic)
  Remove fragments with interference
  Export peak areas or peak area ratio to standard if isotope labeled standards were used

## Slide 30: Data Independent Acquisition (DIA or SWATH)
DIA or Sequential Windowed Acquisition of all Theoretical Fragment Ion Mass Spectra (SWATH)
Measure all fragment ions for all precursors within a limited mass range
Can analyze thousands of peptides in MS2 in one single run
Need known fragmentation patterns and RT for data analysis
Notes: So what if we have 1000’s rather than 50-100 proteins we want to quantify in MS2

## Slide 31: “SRM” on “All”
Precursor m/z
Precursor m/z
SWATH video - https://www.youtube.com/watch?v=VZAZtA_qEbg&feature=youtu.be&t=87

## Slide 32: Advantages of DIA over SRM / PRM
  DIA data analysis assays can be created after samples are run
  Data can be re-analyzed at later stage when more assays are available
  Can detect and quantify thousands of peptides (SRM approx. 100) in one run.
  However, less sensitive than SRM

## Slide 33: DDA vs DIA vs SRM

## Slide 34: DIA data analysis
  Need for spectral libraries to identify peptide peaks
  Fragmentation spectra with relatative fragment intensities
  Indexed Retention Time (iRT)
  Statistical analysis to exclude miss identified peptides and proteins
  http://www.openswath.org/en/latest/

## Slide 35: Tissue based map of the human proteome

## Slide 36: Classification of the human proteome

## Slide 37: Analysis of Tissue elevated proteins

## Slide 38: Generation of metabolic models

## Slide 40: Proteomics and transcriptomics analysis of human tissues

## Slide 41
Proteomics and transcriptomics expressions in human tissues

## Slide 42
Correlations between Proteomics and transcriptomics expressions